## Slide 1: Changes to standards March 2026 Interactive briefing slide deck
Changes in the March 2026 standards update
Draft standards scheduled for consultation
Draft standards scheduled to be published in June 2026
Changes to standards March 2026

## Slide 2: Changes in the March 2026 standards update
2
3 standards
1 standard and 1 guidance note
1 technical note
1 new guidance note
1 guidance note and multiple Rule Book modules updated
Changes to standards March 2026
2 standards and
1 guidance note

## Slide 3
One new Plant technical note has been published in the March Standards Catalogue
TN4300 Issue 1 - Key Plant Principles
Changes to standards March 2026

## Slide 4
This document is intended to be used by:
Suppliers
Overview This technical note relates to RIS-1530-PLT Issue 7.2 On-Track Plant, Trolleys and Associated Equipment and RIS-1710-PLT Issue 2.1 Engineering Certification of Railborne Plant and the Assessment of Non-Railborne Plant. This technical note is also intended to complement published documents: Key Train Requirements and Key Wagon Maintenance Principles.
Benefits This provides industry with a single document providing general information about using railborne plant and other plant. It provides links to the many other sources of useful information and guidance.
TN4300 Issue 1 Key Plant Principles
Changes to standards March 2026

## Slide 5: One new Rolling Stock standard has been published in the March Standards Catalogue
5
Two Rolling Stock standards have been updated in the March Standards Catalogue
RIS-2747-RST Issue 2 - Functioning and Control of Exterior Doors on Passenger Vehicles
RIS-2716-RST Issue 1 - Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem
Changes to standards March 2026
GMRT2113 Issue 2 - Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem

## Slide 6
6
This document is intended to be used by:
Railway Undertakings | Assessment bodies | Suppliers
Overview GMRT2113 Issue 1 Rolling Stock Subsystem and Interfaces to DC Energy Subsystem contained requirements that do not meet the criteria to be classified as National Technical Rules (NTRs). Requirements in GMRT2113 Issue 1 that were valid and useful but cannot be NTRs have been retained in
RIS-2716-RST Issue 1.
Benefits The requirements in this standard provide greater flexibility in their application by removing prescriptive elements for DC rolling stock subsystems that lacked consistent national relevance. The publication of this document (along with GMRT2113 Issue 2, GLRT1212 Issue 2 DC Energy Subsystem and Interfaces to Rolling Stock Subsystem and RIS-1852-ENE Issue 1 DC Energy Subsystem and Interfaces to Rolling Stock Subsystem) provides an estimated overall benefit to industry in excess of £330,000 over five years.
RIS-2716-RST Issue 1 Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem
Changes to standards March 2026

## Slide 7
7
This document is intended to be used by:
Railway Undertakings | Assessment bodies | Suppliers
Overview The content of GMRT2113 has been revised to take account of insights that have arisen from research and requests from industry. GMRT2113 Issue 1 contained some requirements that did not meet the criteria to be classified as NTRs but were useful; these have been transferred to RIS-2716-RST Issue 1 Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem. Guidance that remains useful in the associated Guidance Note GMGN2613 Issue 2 Guidance on Rolling Stock Subsystem and Interfaces to DC Energy Subsystem has also been updated with additional good practice and included in GMRT2113 Issue 2 and RIS-2716-RST Issue 1, where appropriate.
Benefits Key benefits of these changes include a removal of requirements regarding aspects which did not have a reliable value on a national basis. The publication of this document (along with GLRT1212 Issue 2 DC Energy Subsystem and Interfaces to Rolling Stock Subsystem, RIS-2716-RST Issue 1 and RIS-1852-ENE Issue 1 DC Energy Subsystem and Interfaces to Rolling Stock Subsystem) provides an estimated overall benefit to industry in excess of £330,000 over five years.
GMRT2113 Issue 2 Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem
Changes to standards March 2026

## Slide 8
8
This document is intended to be used by:
Suppliers | Railway Undertakings | Infrastructure Managers
Overview The revised standard includes new technologies, such as light curtains and sensitive edge, and has been structurally aligned with BS EN 14752:2019+A1:2021 Railway applications – Bodyside entrance systems for rolling stock. Additionally, the relevant content from GOOTS303 Issue 1 Secondary Door Locking – Operational Requirements has been incorporated as Appendix J.
Benefits The standard promotes good practice, enhancing safety by reducing passenger entrapment risks, and the improvement of operational performance through the use of technologies such as assisted braking and door opening systems.
RIS-2747-RST Issue 2 Functioning and Control of Exterior Doors on Passenger Vehicles
Changes to standards March 2026

## Slide 9: One Control, Command and Signalling standard has been updated in the March Standards Catalogue
GEGN8611 Issue 2 - Guidance on the Application of the Control, Command and Signalling NTSN
GERT8402 Issue 4 - ERTMS/ETCS DMI National Requirements
One Control, Command and Signalling guidance note has been updated in the March Standards Catalogue
Changes to standards March 2026

## Slide 10
This document is intended to be used by:
Project Entities | Infrastructure Managers | Railway Undertakings | Assessment bodies
Overview This document provides guidance on the interpretation and application of technical requirements given within the Control, Command and Signalling National Technical Specification Notice (CCS NTSN). The CCS NTSN has been revised and was published in May 2025. Due to this, the CCS NTSN guidance note has been revised to reference the CCS NTSN Issue 2, remove guidance on sections no longer in the CCS NTSN Issue 2, undertake editorial changes and update standard references. This guidance note also includes new content to describe ERTMS/ETCS baseline specifications, system versions and compatibility, related processes and governance, and transition regimes.
Benefits This guidance note closes the gap for industry-agreed guidance in GB for the revised CCS NTSN requirements. It supports duty holders in understanding and applying the CCS NTSN. This could result in benefits of approximately £140,000 over five years by reducing the need for discussion and agreement on legal compliance and assurance, and relevant processes such as error corrections and ETCS and Radio Compatibility Checks.
GEGN8611 Issue 2 Guidance on the Application of the Control, Command and Signalling NTSN
Changes to standards March 2026

## Slide 11
This document is intended to be used by:
Suppliers | Infrastructure Managers | Railway Undertakings
Overview This update introduces new requirements on the conversion and rounding of current train speed digital and release speed digital values in km/h to mph. New guidance on the display of the Lowest Supervised Speed in the Movement Authority (LSSMA) icon in mph has also been included.
New Appendix A sets out scenarios that provide further clarification of the requirements, set out in section 2.1, for the determination of the stored and applied units used by the ERTMS/ETCS onboard to determine the appropriate speed units to be displayed in different operating levels.
Benefits This document will provide a common approach, avoiding individual implementations by industry. Misinterpretation of the standard caused operational problems and resulted in several deviations.
GERT8402 Issue 4 ERTMS/ETCS DMI National Requirements
Changes to standards March 2026

## Slide 12
One new Energy standard has been published in the March Standards Catalogue
RIS-1852-ENE Issue 1 - DC Conductor Rail Energy Subsystem and Interfaces to Rolling Stock Subsystem
One Energy standard has been updated in the March Standards Catalogue
GLRT1212 Issue 2 - DC Conductor Rail Energy Subsystem and Interfaces to Rolling Stock Subsystem
One Energy guidance note has been updated in the March Standards Catalogue
GEGN8575 Issue 2 - Guidance Note on the Management of Electrical Risk Related to Operational Tasks on Electrified Lines
Changes to standards March 2026

## Slide 13
RIS-1852-ENE Issue 1 DC Conductor Rail Energy Subsystem and Interfaces to Rolling Stock Subsystem
Overview This Rail Industry Standard includes requirements regarding short circuiting bars, hook switch operating tools, tunnel emergency circuits and compatibility with heat emissions from trains and position of signals. It also includes requirements regarding areas on GB mainline where a 750 V DC conductor rail system has a fourth rail to enable London Underground rolling stock to operate. The content in this standard can help support compatibility and efficient operation. Some of the requirements from GLRT1212 Issue 1 DC Conductor Rail Energy Subsystem and Interfaces to Rolling Stock Subsystem, as well as relevant and updated content from Guidance Note GLGN1612 Issue 1 Guidance on DC Conductor Rail Energy Subsystem and Interfaces to Rolling Stock Subsystem, have been transferred to this standard.
Benefits The publication of this document (along with GLRT1212 Issue 2, GMRT2113 Issue 2 Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem and RIS-2716-RST Issue 1 Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem) provides an estimated overall benefit to industry in excess of £338,000 over five years. In addition to these benefits, the documents can help support the efficient and timely delivery of future electrification projects.
This document is intended to be used by:
Project Entities | Infrastructure Managers | Suppliers | Designers
Changes to standards March 2026

## Slide 14
GLRT1212 Issue 2 DC Conductor Rail Energy Subsystem and Interfaces to Rolling Stock Subsystem
Overview This standard has been revised to take account of insights that have arisen from research and requests from industry to align with post-EU exit legislation and changes to referenced British Standards. GLRT1212 Issue 1 contained some requirements that do not meet the current criteria to be NTRs but are useful; these have been transferred to RIS-1852-ENE Issue 1 DC Conductor Rail Energy Subsystem and Interfaces to Rolling Stock Subsystem. Requirements regarding short circuit currents, loss of line voltage and conductor rail layout have been removed and become open points in this issue.
Benefits Key benefits of these changes include the removal of requirements regarding aspects which did not have a reliable value on a national basis. The publication of this document (along with GMRT2113 Issue 2 Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem,
RIS-1852-ENE Issue 1 and RIS-2716-RST Issue 1 Rolling Stock Subsystem and Interfaces to DC Conductor Rail Energy Subsystem) provides an estimated overall benefit to industry in excess of £338,000 over five years. In addition to these benefits, the documents can also help support the efficient and timely delivery of future electrification projects.
This document is intended to be used by:
Project Entities | Infrastructure Managers | Suppliers | Designers
Changes to standards March 2026

## Slide 15
GEGN8575 Issue 2 Guidance Note on the Management of Electrical Risk Related to Operational Tasks on Electrified Lines
Overview This updated document provides improved guidance, based on industry feedback, to better assist railway undertakings (RUs) and infrastructure managers (IMs)(station operators) in undertaking a suitable and sufficient risk assessment for day-to-day operational tasks on electrified lines. It can also assist RUs and IMs (station operators) in demonstrating how the relevant legal obligations in The Electricity at Work Regulations 1989 and in the Management of Health and Safety at Work Regulations 1999 are being met.
Benefits The revised guidance note improves clarity whilst continuing to assist organisations in developing a proportionate, suitable and sufficient electrical risk assessment. The improved clarity continues to provide a consistent approach to avoid unnecessarily complex analysis being undertaken,
excessive resources being committed and the incursion of unwarranted costs.
This document is intended to be used by:
Railway Undertakings | Infrastructure Managers
Changes to standards March 2026

## Slide 16: One Traffic Operation and Management guidance note has been updated in the March Standards Catalogue
GOGN3615 Issue 3 - Guidance on the Operation and Traffic Management National Technical Specification Notice (OPE NTSN)
Changes to standards March 2026

## Slide 17
This document is intended to be used by:
Infrastructure Managers | Railway Undertakings
Overview GOGN3615 has been updated to reflect the content of the OPE NTSN Issue 2. It includes references to the relevant standards that will assist users in complying with the OPE NTSN requirements. It also clarifies OPE NTSN content, as requested by industry. The revision took into account consultation comments received during the industry consultation on the industry recommendation for Issue 2 of the OPE NTSN, the recommendations from the
12-month review of GOGN3615 in December 2019, and relevant content from the European Union Agency for Railways Guide for the application of the TSI OPE.
Benefits This guidance note will support users in interpreting the OPE NTSN and choosing how to apply the respective requirements. The updated document has been aligned with legislation, which should reduce the number of enquiries requesting clarification and assistance. It will also reduce the potential for legal claims due to misinterpretation of responsibilities.
GOGN3615 Issue 3 Guidance on the Operation and Traffic Management National Technical Specification Notice (OPE NTSN)
Changes to standards March 2026

## Slide 18
The following Rule Book modules and handbooks have been updated in the March Standards Catalogue
GERT8000-M1 Issue 9 - Dealing with a train accident or train evacuation
GERT8000-M2 Issue 9 - Train stopped by train failure
GERT8000-TW1 Issue 22 - Preparation and movement of trains
Changes to standards March 2026
GERT8000-AC Issue 10 - AC Electrified Lines
GERT8000-HB17 Issue 6 - DC Electrified Lines
GERT8000-DC Issue 8 - DC Electrified Lines
GERT8000-HB16 Issue 7 - AC Electrified Lines

## Slide 19
Key changes
The actions following a train accident in sections 1 and 2 have been extensively revised. Greater emphasis has now been placed on the use of available means of telling the signaller, and the ability to alert drivers by using GSM-R radio. The sooner the signaller and other drivers can be made aware, the more likely it is that further consequences can be avoided. The methods of contacting the signaller are now set out in the order in which they are most likely to be effective as quickly as possible, and in which they are to be used.
After leaving the train, the driver uses a hand danger signal to warn drivers of approaching trains. If it is possible to stop an approaching train, the driver of that train is asked to tell the signaller.
The requirements concerning tunnels and diverging junctions have been changed so that the maximum warning can be given to the driver of any approaching train.
Track-circuit operating clips are not required to be placed after the signaller has been spoken to unless the signaller asks the driver to do so. They must be placed before leaving the driving cab to use the GSM-R radio in another cab, or to speak to the signaller.
More detail is given on the actions to be taken if lines used in both directions are affected.
The use of detonators will be retained for a trial period in some situations when a driver has left the train to contact the signaller.
The requirement for emergency protection on the line the train had been travelling during extended block working has been removed, as the risk this guards against is considered to be extremely small.
GERT8000-M1 Issue 9 Dealing with a train accident or train evacuation
Changes to standards March 2026

## Slide 20
Key changes
Changes have been made to this module as a result of those made to module M1 Dealing with a train accident or train evacuation.
There is no longer any requirement to place emergency protection if a train has failed during extended block working, and therefore all references have been removed from this module.
As a result, the number of locations where the assisting train might meet the driver of the failed train has been reduced.
GERT8000-M2 Issue 9 Train stopped by train failure
Changes to standards March 2026

## Slide 21
Key changes
The rules concerning emergency protection following a train accident and when other trains are put in danger have been reviewed. Changes have been made to section 45.1 of this module that correspond to similar changes made to module M1 Dealing with a train accident or train evacuation.
The actions of a driver on exploding detonators have been changed to include making a REC to tell the signaller and other drivers about a possible hazard. A new rule has been added to state that this also applies if a hand danger signal is seen unexpectedly when not already bringing a train to a stand as a result of receiving a REC.
Section 45.1 now includes revised versions of the existing instructions in a new sub-section a) ‘When trains in the opposite direction are put in danger' as they are only relevant to that situation. A new sub-section b) ‘When trains in the same direction are put in danger' has been introduced, as the question of a hazard to a train on another running line used in the same direction has not previously been catered for.
Section 45.1 a) now includes a requirement to use any other means of direct communication available within the driving cab to tell the signaller if unable to make a REC.
To avoid any ambiguity, it is now stated that in moving forward to the 1 1/4 mile point, a driver must not pass any signal at danger unless already having been authorised to do so.
Once the driver has stopped at the 1 1/4 mile point, the signaller can allow the train to proceed on its journey normally if the signaller can confirm no train is approaching. Whilst this can be the case under the existing rules, it is not made clear.
GERT8000-TW1 Issue 22 Preparation and movement of trains
Changes to standards March 2026

## Slide 22
Key changes
Having stopped at this location, the placing of a track-circuit operating clip is only required if the signaller has not yet been spoken to, or if requested by the signaller.
Using GSM-R from another driving cab has been added as another means of contacting the signaller from that location.
Section b) is completely new and requires the driver to stop the train as soon as possible and to contact the signaller as soon as possible. The driver's actions are then similar to those in module M1, and if it is necessary to leave the train before the signaller has been spoken to, the driver must show the hazard warning indication at the rear of the train.
The requirement to place detonators is retained for a trial period in three situations.
GERT8000-TW1 Issue 22 continued Preparation and movement of trains
Changes to standards March 2026

## Slide 23
GERT8000-AC Issue 10 AC Electrified Lines
Changes to standards March 2026
Key changes The modules and handbooks relating to AC and DC electrified lines have been reviewed to include a number of changes that had been proposed by the industry.
The changes include the following:
Descriptions of electrification systems.
Definitions and terminology.
Emergency switch-off arrangements.
Additional diagrams.
Actions following an OLE-related incident.

## Slide 24
GERT8000-DC Issue 8 DC Electrified Lines
Changes to standards March 2026
Key changes The modules and handbooks relating to AC and DC electrified lines have been reviewed to include a number of changes that had been proposed by the industry.
The changes include the following:
Descriptions of electrification systems.
Definitions and terminology.
Emergency switch-off arrangements.
Additional diagrams.

## Slide 25
Key changes The modules and handbooks relating to AC and DC electrified lines have been reviewed to include a number of changes that had been proposed by the industry.
The changes include the following:
Descriptions of electrification systems.
Definitions and terminology.
Emergency switch-off arrangements.
Additional diagrams.
Actions following an OLE-related incident.
GERT8000-HB16 Issue 7 AC Electrified Lines
Changes to standards March 2026

## Slide 26
GERT8000-HB17 Issue 6 DC Electrified Lines
Changes to standards March 2026
Key changes The modules and handbooks relating to AC and DC electrified lines have been reviewed to include a number of changes that had been proposed by the industry.
The changes include the following:
Descriptions of electrification systems.
Definitions and terminology.
Emergency switch-off arrangements.
Additional diagrams.

## Slide 27
27
GEGN8601 Issue 1 General Guidance on the Implementation of NTSNs
Overview This new guidance note provides general information on topics that are relevant to multiple National technical Specification Notices (NTSNs). It covers the regulatory context, roles and responsibilities, the links between NTSNs and other parts of the framework, implementation and conformity assessment. This new document combines, updates and fills gaps in existing guidance, to put relevant industry-agreed information in a single place.
Benefits This guidance is estimated to provide the industry with benefits ranging from £80k to £200k over the next five years. This document should support more efficient delivery of projects through reduced volume of discussions and questions and may also produce potential cost savings for projects through correct application, rather than misinterpretation requiring rework.
This document is intended to be used by:
Railway Undertakings | Project Entities | Assessment bodies
Changes to standards March 2026

## Slide 28
Draft standards scheduled for publishing in June 2026
Changes to standards March 2026
Traffic Operation and Management RIS-3780-TOM Issue 3 Operational Requirements for GSM-R Radio

## Slide 29
Draft standards scheduled for consultation in March 2026
Infrastructure RIS-7710-INS Issue 1 Wayfinding and Tactile Navigation
Infrastructure RIS-7709-INS Issue 1 Station Facilities
Infrastructure RIS-7702-INS Issue 2 Lighting at Stations
Infrastructure RIS-7701-INS Issue 1 (withdrawal) Rail Industry Standard for Automatic Ticket Gates at Stations
Infrastructure RIS-7700-INS Issue 4 Station Infrastructure
Changes to standards March 2026

## Slide 30
Draft standards scheduled for consultation in March 2026 continued
Rolling Stock GOGN3681 Issue 1 Operation of Vehicles with Traction Batteries
Rolling Stock RIS-2781-RST Issue 1 Engineering Design of Vehicles with Traction Batteries and their Dedicated Charging Systems
Changes to standards March 2026
Control, Command and Signalling RIS-8060-CCS Issue 2 Engineering Requirements for Dispatch of Trains from Platforms

## Slide 31
Draft standards scheduled for consultation in May 2026
Rolling Stock RIS-2731-RST Issue 1 Braking Systems of Rail Vehicles
Rolling Stock GMRT2045 Issue 5 Compatibility Requirements for Braking Systems of Rail Vehicles
Changes to standards March 2026
Rolling Stock RIS-2713-RST Issue 2 System Requirements for the Introduction and Operation of Multi-Mode Rolling Stock

## Slide 32
Draft standards scheduled for consultation in August 2026
Control, Command and Signalling RIS-0796-CCS Issue 2 Train to Infrastructure RFID Compatibility
Changes to standards March 2026

## Slide 33
Draft standards scheduled for consultation in September 2026
Control, Command and Signalling GKGN0602 Issue 2 Guidance on Train Rooftop Antenna Positioning
Traffic Operation and Management RIS-3119-TOM Issue 4 Accident and Incident Investigation
Traffic Operation and Management RT3119-B Issue 10 Provisional SPAD Data Collection Form (Railway Undertaking)
Data, Systems and Telematics RIS-6703-DST Issue 1 Telematics Message Exchanges between Railway Undertakings and Infrastructure Managers
Changes to standards March 2026

## Slide 34
Draft standards scheduled for consultation in January 2027
Infrastructure GIGN5633 Issue 2 Recommendations for the Risk Assessment of Buffer Stops and End Impact Walls
Changes to standards March 2026

## Slide 35
Draft standards scheduled for consultation in May 2027
Changes to standards March 2026
Control, Command and Signalling RIS-0799-CCS Issue 2 ERTMS/ETCS Onboard Subsystem Requirements