## Slide 1: Rule Book changes

## Slide 2: About these
Use this style of slide when your content is just plain text.
Changing the text in the footer:
In the Ribbon, select View > Slide Master.
In the Slide Master tab scroll up to the Number 1 master slide.
You can change the footer text in here.
When you have finished change your Presentation View to Normal.
These are a number of changes that have been made to the Rule Book
They will be published in September and will come into force on 5 December
For the more complex changes, a series of videos have been produced
These slides describe the other changes
Notes: We have updated the requirements for managing defective on-train equipment so that they permit a more proportionate approach to improve the performance when trains are defective. By consideringed whole system risk certain requirements concerning when passengers are detrained , introduces additional controls for duration and speed for defective passenger trains to continue to manage risk, but these are more proportionate and should improve the performance of defective trains have been relaxed, but additional controls on speed and duration have been introduced as a more effective means of managing risk. Read the update.

## Slide 3: Flexible Train Arrival Point (FTAP)
When previously agreed and published, a possession can be taken around an engineering train or on-track machine standing at a specified signal or block marker.
When there is no signal conveniently placed close to the site of work, a new arrangement is being introduced for the train to be located at an FTAP. This can also apply when a protection zone (PZ) is to be taken around a train.
To indicate the location of the FTAP, a series of three countdown markers will be provided, and an FTAP ‘Stop’ sign to show where the train must stop.
Handbooks 11 and 12 and module T3 have been changed to refer to this and module TW1 section 40 has been changed to include a train stopping in section at an FTAP as another situation the driver must tell the signaller about.

## Slide 4: Protection zone (PZ)
With the introduction of PZs, as described in detail in a video, a number of other changes have been made to modules and handbooks.
A line can also be considered as blocked if it is within a PZ. This has been shown in handbook 6, 7.
Handbook 19 and module TS11 have been changed. If signalling equipment affected is within the area of a PZ, but will be restored to normal use before the PZ is given up, this is another occasion when Form RT3187 does not have to be used.
Module OTM has been changed to show a PZ as another situation in which an OTM can work outside a possession, and another situation in which wrong-directions movements can be made outside a possession.
Modules TS1 and TW1 now include an ES or SWL who has set up a PZ as a person who can ask for an adjacent line to be blocked to protect staff walking or working.
Module TW5 now allows the AWS or TCA to be isolated during a journey, if it is necessary to isolate either of these on an on-track machine that is to work within a PZ.
Module TW7 now allows wrong-direction movements to be made within a PZ, as long as the signaller has agreed this in advance with the ES or SWL.

## Slide 5: Module AC
As well as the changes concerning examination of the OLE, pantograph and the train, which are described in a video, there are three other changes.
Section 3.3 – Reporting objects or defects to the ECO. At present this requires anyone to report the fact to the ECO. This has been changed to say that if you do not normally speak directly to the ECO, you must report this to the signaller. This more correctly reflects what would happen in practice.
Section 3.3 refers to not touching any red bonds. These are now not always coloured red, and the rule has been changed to say that no bonds should be touched.
Section 12.1 has been changed. If an ADD operation occurs, but the line light does not go out on a train with more than one raised pantograph it is no longer necessary to stop the train immediately. As this would indicate that at least one pantograph is in contact with the OLE, the train can continue to a location more suitable for the train to be dealt with, and so avoid the train being stranded in an inconvenient location.

## Slide 6: Module M1 dealing with a train accident or train evacuation
What to do after a train accident
As it is important that the signaller is told about the accident as soon as possible so that it can be protected and the traction current switched off, the rule in module M1 has been changed so that the driver must do this before finding out which lines are obstructed.

## Slide 7: Trains colliding with obstructions
Following an accident in which a train struck bridge debris and was allowed to go forward without full consideration of any restrictions that should be applied, the rules in module M3 following this type of accident have been changed.
The driver must speak to the train operator's control if it is possible that there may have been damage that would affect any further safe movement of the train, or that damage may have increased the height or width of the train.
The driver will then be told either that the train can proceed, possibly subject to restrictions, or that the train must not proceed until a rolling stock technician has examined the vehicle affected and given permission for the train to proceed, together with any restrictions that must be applied.
The driver must tell the signaller, including whether any restrictions such as a maximum speed will apply.
The driver must not take this as permission to proceed until after the signaller has spoken to Operations Control, who have given permission for the movement to take place, and the signaller gives the driver permission, including any instructions from Operations Control.

## Slide 8: Ground position-light signals
New rules have been added in module S5 to explain that when a driver is authorised to pass a signal at danger, the authority is to proceed as far as the next main aspect stop signal, ignoring the aspects of any intervening ground position-light signals.
If a driver is only being authorised to proceed as far as a ground position-light signal the signaller will state this.
There have been cases in which this has not be made clear, and a train has proceeded further than intended.

## Slide 9: Passing a signal at danger with authority
In module S5 section 4.4 has been changed to allow a driver to increase speed as appropriate from the reduced speed after sighting a proceed aspect at the signal after the one passed with authority, unless the signaller has specified a need to continue at caution as far as that signal.
The present rule refers to the possibility of another train being within the signal section and is based on hazards associated with procedures and equipment that no longer apply.

## Slide 10: Intermediate block home signals
The authority for a driver to pass at danger an intermediate block home signal when unable to contact the signaller has been withdrawn from section 7 of module S5.
With GSM-R radio available throughout the network and being of proven reliability, it is much less likely that the driver would be unable to contact the signaller by any means than in former years.

## Slide 11: Driver passing a signal at danger or an EoA without authority
Module S5 has been changed to allow a train which has passed a signal at danger to be moved to a more convenient location to clear a junction or station approach and avoid obstructing other trains.
This can only be done as long as:
    The driver is prepared to make the movement.
    The driver considers that there is no defect that would make it unsafe to move the train.
    The movement will not proceed beyond another main aspect stop signal or block marker.

## Slide 12: Travelling in driving cabs
Because of changes to the arrangements for issuing cab passes there are changes to module G1 and handbook 1.
Travelling in the driving cab is only allowed in connection with duties shown in the Rule Book or when the person has authority to do so. This explains the situation more correctly.
The driver must be told why it is necessary to travel in the cab.
The driver must be told if the holder has a PTS competence but does not have all the necessary equipment to go on or near the line.
Additional written permission must be shown to travel in the cab of a train carrying high consequence dangerous goods.
The holder must check with the driver whether any mobile electronic devices require to be switched off.

## Slide 13: Module TS1 - clarifications
Clarifications have been made in module TS1 to clarify the meaning of the regulations.
A line blockage can only be granted by the signaller who controls the protecting signal.
In some cases the signaller must be requested to arrange the additional protection.
Module TS1 has been amended to refer to finding out whether the points being worked on have been secured or the point machine isolated, as well as to explain that the requirements do not apply when a line blockage has been taken.